## Slide 1
01 / THE CONTEXT & PROBLEM
THE GRID IS BECOMING
LESS PREDICTABLE.
Renewables fluctuate. Demand moves. Flexibility is uncertain. Every intervention has consequences.
GRIDSENTINAL | Adaptive, Self-Verifying Energy Intelligence
Yuva Yodha Energy Tech 2026 | Schneider Electric
01 / 11
RENEWABLES
DEMAND
DER ASSETS
GRID STATE
5,196 nodes
1,871 loads
→
UNCERTAINTY
intervals, not
single numbers
→
DECISION
act or hold
MODELED ON REAL DATA · SMART-DS v1.0
5,196
nodes
1,871
customer loads
1,216
PV arrays
93
batteries
35,040
15-min intervals
Source: SMART-DS v1.0 feeder p1uhs0_1247, AUS/P1U 2018; verified ingestion, 359 files SHA-256 checked.

## Slide 2
02 / THE CRITICAL INDUSTRY GAP
PREDICTION IS ONLY
THE FIRST PROBLEM.
Why naive automation fails: four interacting challenges, measured on a real feeder.
GRIDSENTINAL | Adaptive, Self-Verifying Energy Intelligence
Yuva Yodha Energy Tech 2026 | Schneider Electric
02 / 11
01
VARIABLE DEMAND
Household load on a 15-minute grid is smooth at 15 min but error grows with horizon: MAE 0.40 kW at 15 min vs 2.43 kW at 24 h for persistence.
02
RENEWABLE INTERMITTENCY
Solar ramps concentrate error. Without a weather forecast, day-ahead PV error is 74.3 kW against 8.57 kW with weather at the origin.
03
UNCERTAIN FLEXIBILITY
0 of 8 physical flexibility dimensions are supported by the data. A statistical proxy exists, but it is not dispatchable capacity.
04
UNCHECKED DECISION RISK
A point forecast hides its own reliability. The default constant-width interval fails 11 of 12 coverage cells on this feeder.
FORECAST ERROR
+
HIDDEN UNCERTAINTY
+
UNKNOWN CAPABILITY
+
PHYSICAL CONSEQUENCES
=
NAIVE AUTOMATION IS UNSAFE

## Slide 3
03 / PROPOSED SOLUTION
MEET GRIDSENTINAL.
An adaptive, self-verifying energy intelligence system for renewable-integrated distributed networks.
GRIDSENTINAL | Adaptive, Self-Verifying Energy Intelligence
Yuva Yodha Energy Tech 2026 | Schneider Electric
03 / 11
“Don't just predict the grid.
Verify what happens next.”
Uncertainty, capability limits and decision verification are first-class parts of the pipeline, not reporting dashboards.
FORECAST
↓
UNCERTAINTY
↓
FLEXIBILITY
↓
DECISION
↓
VERIFY
Shaded: operational today. Outlined: designed, next on the roadmap.
GridSentinal console: 48-hour demand forecast with calibrated 90% interval, recorded model output on SMART-DS telemetry.

## Slide 4
04 / SYSTEM ARCHITECTURE
FROM TELEMETRY
TO TRUSTED DECISION.
A layered, evidence-based pipeline with explicit operational status for every layer.
GRIDSENTINAL | Adaptive, Self-Verifying Energy Intelligence
Yuva Yodha Energy Tech 2026 | Schneider Electric
04 / 11
DATA
OPERATIONAL
→
DATA QUALITY
OPERATIONAL
→
FORECASTING
OPERATIONAL
→
EXPERTS
OPERATIONAL
→
UNCERTAINTY
OPERATIONAL
→
FLEXIBILITY
STATISTICAL PROXY
→
DECISION
DESIGNED
→
ASSURANCE
DESIGNED
WHAT RUNS TODAY
Data ingestion and reality validation, multi-expert forecasting, and calibrated uncertainty are operational end to end on 179,520 sealed test rows.
WHAT COMES NEXT
Flexibility today is a statistical proxy (a data blocker is recorded). The decision, red-team, twin and assurance layers are designed and specified, not implemented.
Design contract: no layer is marked operational that has not been run end to end against the sealed test split. Roadmap components are labelled as such throughout this deck.

## Slide 5
05 / PROBABILISTIC INTELLIGENCE
KNOW WHAT YOU DON'T KNOW.
A point forecast fails silently. A calibrated interval says which rows to trust, and which to suppress.
GRIDSENTINAL | Adaptive, Self-Verifying Energy Intelligence
Yuva Yodha Energy Tech 2026 | Schneider Electric
05 / 11
Chart: kW
| 06:00 | 14:00 | 22:00 | 06:00 | 14:00 | 22:00
Upper 90% | 0.7029 | 0.9814 | 0.9828 | 1.0544 | 1.5693 | 2.1637 | 2.1704 | 1.8755 | 2.0517 | 2.5147 | 1.5177 | 1.1123 | 0.9067 | 1.5138 | 1.1192 | 1.5137 | 1.4275 | 0.4674 | 0.6682 | 0.3653 | 0.4552 | 0.5722 | 0.6102 | 0.7882 | 0.9633 | 0.8765 | 0.958 | 1.3149 | 1.3878 | 2.4394 | 3.5803 | 4 | 5.2218 | 4.4504 | 3.2449 | 3.2552 | 1.534 | 1.4526 | 1.1505 | 0.984 | 1.2661 | 0.7136 | 0.8191 | 0.7053 | 0.7717 | 0.6974 | 0.8039 | 1.1237
Point forecast | 0.504 | 0.5723 | 0.5629 | 0.3617 | 0.3646 | 0.3267 | 0.3201 | 0.4573 | 0.9085 | 1.2464 | 0.8861 | 0.6988 | 0.4884 | 0.7509 | 0.6722 | 1.0606 | 0.9682 | 0.2719 | 0.2802 | 0.2779 | 0.3255 | 0.3556 | 0.3737 | 0.3622 | 0.4057 | 0.4118 | 0.3645 | 0.5313 | 0.5077 | 1.0045 | 1.5232 | 1.8647 | 2.4343 | 2.403 | 2.0706 | 1.9089 | 0.7882 | 0.8289 | 0.7814 | 0.6851 | 0.8349 | 0.3797 | 0.4737 | 0.4284 | 0.511 | 0.4973 | 0.5288 | 0.5531
Lower 90% | 0.305 | 0.1631 | 0.143 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.2545 | 0.2853 | 0.0701 | 0 | 0.2251 | 0.6076 | 0.5089 | 0.0763 | 0 | 0.1905 | 0.1957 | 0.1389 | 0.1372 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.3556 | 0.8962 | 0.5627 | 0.0424 | 0.2052 | 0.4122 | 0.3863 | 0.4036 | 0.0458 | 0.1283 | 0.1514 | 0.2502 | 0.2972 | 0.2537 | 0
48-hour window, 1-hour-ahead horizon, asset load_p1ulv14763. Recorded output, sealed test split.
90.2%
coverage at h=1
89.7%
coverage at h=4
+0.67
width-error rank corr.
FLEXIBILITY WITHOUT FICTION
PHYSICAL
UNKNOWN
0 of 8 flexibility dimensions supported by the dataset (G-01).
STATISTICAL
AVAILABLE
Behavioural envelope from 1,871 consumption series; rank correlation with error confirms signal.
ASSUMED
SCENARIO ONLY
Dispatch scenarios stay clearly labelled as assumptions.
Historical consumption behaviour is not automatically dispatchable capacity.

## Slide 6
06 / DECISION ASSURANCE ENGINE
BEFORE IT ACTS,
IT TRIES TO BREAK THE DECISION.
Instead of asking only what the system should do, GridSentinal asks whether the action survives hostile evaluation.
GRIDSENTINAL | Adaptive, Self-Verifying Energy Intelligence
Yuva Yodha Energy Tech 2026 | Schneider Electric
06 / 11
01
PROPOSE
Optimizer drafts a candidate action from forecasts, uncertainty, flexibility and constraints.
02
RED TEAM
Adversarial scenarios attack failure modes: when is it unsafe, ineffective or suboptimal?
03
SIMULATE
An independent digital twin replays the action against physics and compares outcomes.
04
ASSURE
The assurance gate approves, rejects, or re-optimizes, with human-in-the-loop fallback.
05
EXECUTE
Only after verification. Outcomes return to the system as performance data.
STATUS. The assurance sequence is a designed architecture (roadmap), not shipped functionality. What is shipped today is the discipline it will enforce: sealed data splits, pre-registered success bars, and negative results recorded instead of engineered around.
“An action is not executed because it was proposed. It is executed because it survived.”

## Slide 7
07 / TECHNICAL APPROACH
A RESEARCH PIPELINE,
NOT A SINGLE MODEL.
Five layers, each with an explicit implementation status and a measurable exit criterion.
GRIDSENTINAL | Adaptive, Self-Verifying Energy Intelligence
Yuva Yodha Energy Tech 2026 | Schneider Electric
07 / 11
LAYER 1
DATA
SMART-DS v1.0, 15-minute native resolution, 359 files checksummed
IMPLEMENTED
LAYER 2
FORECASTING
Persistence, Hist-GBM, temporal TCN; fixed weighted ensemble ships
IMPLEMENTED
LAYER 3
PROBABILISTIC INTELLIGENCE
Split-conformal intervals, six methods calibrated, one published procedure
IMPLEMENTED
LAYER 4
FLEXIBILITY
Capability audit, behavioural envelope, physical gaps recorded
PARTIAL
LAYER 5
DECISION
Optimization, red team, digital twin, assurance gate
DESIGNED
TECH STACK
Python 3.12 · PyTorch (CPU-deterministic) · scikit-learn · OpenDSS · pytest (1,235 tests)

## Slide 8
08 / RESEARCH & EXPERIMENTAL EVIDENCE
WE TESTED THE IDEA.
WE DIDN'T JUST DEMO IT.
1,235 tests passing, 29 registered experiments, and negative results recorded rather than engineered around.
GRIDSENTINAL | Adaptive, Self-Verifying Energy Intelligence
Yuva Yodha Energy Tech 2026 | Schneider Electric
08 / 11
QWEN
Language-model specialization
NEGATIVE
ROUTER
Learned expert routing
NEGATIVE
UNCERTAINTY
Conformal calibration
VERIFIED
FLEXIBILITY
Physical capability audit
NO PHYSICAL SUPPORT
ABLATION
Feature contribution
TARGET-DEPENDENT
Chart: 
| Persistence | Hist-GBM | Temporal TCN | Learned router | Fixed ensemble | Oracle bound
MAE at 24 h (kW) | 2.4343 | 1.5737 | 1.651 | 1.56 | 1.5399 | 0.9942
Demand forecast error at 24 h ahead (kW MAE, sealed test split, 179,520 rows). The fixed weighted ensemble ships; the oracle bounds what perfect routing would reach.
WHAT THE NUMBERS SAY
+0.66 to +0.71
rank correlation between interval width and realized error at every horizon
4.2x to 4.8x
mean error carried by the widest tenth of prediction intervals
11 of 12
coverage cells failed by the default constant-width interval (recorded, not hidden)

## Slide 9
09 / INNOVATION & CHALLENGE ALIGNMENT
WHAT ACTUALLY MAKES
GRIDSENTINAL DIFFERENT?
A direct causal mapping from the Grid Reliability challenge needs to system capabilities.
GRIDSENTINAL | Adaptive, Self-Verifying Energy Intelligence
Yuva Yodha Energy Tech 2026 | Schneider Electric
09 / 11
CHALLENGE NEED
GRIDSENTINAL RESPONSE
VALUE
RENEWABLE INTERMITTENCY
→
15-min multi-expert nowcasting plus a calibrated 24 h horizon with conformal error envelopes.
→
Ramp foresight for DISCOMs; no blind generation shortfalls.
DER & STORAGE COORDINATION
→
Flexibility capability audit and behavioural envelopes; refuses unverified dispatch.
→
No over-commitment penalties; only physically supported assets move.
TECHNICAL LOSSES & PHYSICS
→
Formal energy contract with loss modeling; OpenDSS twin validates power flow.
→
Dispatch actions close physically; thermal stress prevented.
AUTONOMOUS GRID SAFETY
→
Red-team stress testing plus a decision-assurance gate with human fallback.
→
Zero unchecked automated decisions; verifiable operational safety.
SYSTEM-LEVEL INNOVATION. GridSentinal treats uncertainty, capability limits and verification as first-class parts of energy intelligence.

## Slide 10
10 / VALUE CREATION & ROADMAP
FROM LAB EVIDENCE
TO INDUSTRIAL DEPLOYMENT.
A clear line between the completed research foundation and industrial scaling.
GRIDSENTINAL | Adaptive, Self-Verifying Energy Intelligence
Yuva Yodha Energy Tech 2026 | Schneider Electric
10 / 11
EXPECTED IMPACT
GRID RELIABILITY
Pre-emptive mitigation of solar ramps and evening peaks through calibrated forecast bounds.
DISCOM OPERATIONS
Visibility into demand behaviour; statistical proxies never mistaken for dispatchable capacity.
OPERATIONAL SAFETY
Verified decisions instead of blind automation; every consequential action confirmed.
ENERGY-AWARE MLOPS
Model performance judged by operational consequence, with deployment gates.
ROADMAP
01
PROVEN FOUNDATION
COMPLETE
Data validation, forecasting ensemble, calibrated uncertainty, flexibility audit, feature ablation.
02
DECISION & VERIFICATION
NEXT
Optimization, digital twin, red team, assurance gate; ADMS / DERMS integration paths.
03
INDUSTRIAL SCALING
FUTURE
Hardware-in-the-loop testing, MLOps deployment gates, multi-feeder operation.

## Slide 11
11 / TEAM & CONCLUSION
BUILDING THE GRID'S
INTELLIGENCE LAYER.
The Unsupervised Suspects · Yuva Yodha Energy Tech Hackathon 2026, Schneider Electric.
GRIDSENTINAL | Adaptive, Self-Verifying Energy Intelligence
Yuva Yodha Energy Tech 2026 | Schneider Electric
11 / 11
Pratham Kapoor
A028
Saransh Naruka
A071
Ritesh Pandey
A086
Moinuddin Shaikh
A093
Javin Sharma
B091
The GridSentinal public experience and console: github.com/PrathamKapoor/GridSentinal
GRID SENTINAL
DON'T JUST AUTOMATE THE GRID.
MAKE IT THINK BEFORE IT ACTS.
github.com/PrathamKapoor/GridSentinal
Proprietary. All rights reserved. Research system; no production deployment is claimed.